# Modelling the Z80 instructions on the 6502
## The Z80, 6502 register correspondence
Z80	6502
A, AF	A, SR
B, C, BC	zc+1, zc, zc
D, E, DE	ze+1, ze, ze
H, L, HL	zl+1, zl, zl
SP
IX	zx
IY	zy

zc, ze, zl, zx, zy are words in the zero page memory.
zs is a word for temporary values in the ZP.
XR is always 0 - this allows to have faster (HL)-based addressing

The 6502 and Z80 have several architectural differences which makes the emulation of several the Z80's features almost impossible:
- The stack pointer of the 6502 has its high byte always set to 1 but SP of the Z80 has 16 bits;
- The 6502 load instructions (LDA, TXA, LDY, PLA, ...) change SF and ZF, the Z80 load instructions don't change flags;
- The 6502 has the decimal mode and the Z80 has decimal correction instruction (DAA);
- The 6502 doesn't have parity, half-carry and subtraction flags;
- The 6502 uses the inverted carry flag for subtractions and comparisons;
- The 6502 instructions JSR and RET work with a stack a bit differently than the Z80 instructions CALL and RET;
- The 6502 has nothing similar to the Z80 instructions HALT, RETN and IM or to registers R and I;
- The Z80 instruction RETI is unique in the processor world;
- The 6502 doesn't have a special address space for input and output.

## The 6502 instructions for the Z80 instructions

Z80					6502			comments
instruction		code	size	ticks	instructions	size	ticks
LD	A,A	7F	1	4	NOP	1	2
LD	A,B	78	1	4	LDA zc+1	2	3
LD	A,C	79	1	4	LDA zc	2	3
LD	A,D	7A	1	4	LDA ze+1	2	3
LD	A,E	7B	1	4	LDA ze	2	3
LD	A,H	7C	1	4	LDA zl+1	2	3
LD	A,L	7D	1	4	LDA zl	2	3
LD	A,(HL)	7E	1	7	LDA (zl,X)	2	6
LD	A,(BC)	0A	1	7	LDA (zc,X)	2	6
LD	A,(DE)	1A	1	7	LDA (ze,X)	2	6
LD	A,(word)	3A word	3	13	LDA word	3	4
LD	A,(IX+byte)	DD 7E byte	3	19	LDY #byte LDA (zx),Y	4	7-8
LD	A,(IY+byte)	FD 7E byte	3	19	LDY #byte LDA (zy),Y	4	7-8
LD	B,A	47	1	4	STA zc+1	2	3
LD	B,B	40	1	4	NOP	1	2
LD	B,C	41	1	4	LDY zc STY zc+1	4	6
LD	B,D	42	1	4	LDY ze+1 STY zc+1	4	6
LD	B,E	43	1	4	LDY ze STY zc+1	4	6
LD	B,H	44	1	4	LDY zl+1 STY zc+1	4	6
LD	B,L	45	1	4	LDY zl STY zc+1	4	6
LD	B,(HL)	46	1	7	TAY LDA (zl,X) STA zc+1 TYA	6	13
LD	B,(IX+byte)	DD 46 byte	3	19	PHA LDY #byte LDA (zx),Y STA zc+1 PLA	8	17-18
LD	B,(IY+byte)	FD 46 byte	3	19	PHA LDY #byte LDA (zy),Y STA zc+1 PLA	8	17-18
LD	C,A	4F	1	4	STA zc	2	3
LD	C,B	48	1	4	LDY zc+1 STY zc	4	6
LD	C,C	49	1	4	NOP	1	2
LD	C,D	4A	1	4	LDY ze+1 STY zc	4	6
LD	C,E	4B	1	4	LDY ze STY zc	4	6
LD	C,H	4C	1	4	LDY zl+1 STY zc	4	6
LD	C,L	4D	1	4	LDY zl STY zc	4	6
LD	C,(HL)	4E	1	7	TAY LDA (zl,X) STA zc TYA	6	13
LD	C,(IX+byte)	DD 4E byte	3	19	PHA LDY #byte LDA (zx),Y STA zc PLA	8	17-18
LD	C,(IY+byte)	FD 4E byte	3	19	PHA LDY #byte LDA (zy),Y STA zc PLA	8	17-18
LD	D,A	57	1	4	STA ze+1	2	3
LD	D,B	50	1	4	LDY zc+1 STY ze+1	4	6
LD	D,C	51	1	4	LDY zc STY ze+1	4	6
LD	D,D	52	1	4	NOP	1	2
LD	D,E	53	1	4	LDY ze STY ze+1	4	6
LD	D,H	54	1	4	LDY zl+1 STY ze+1	4	6
LD	D,L	55	1	4	LDY zl STY ze+1	4	6
LD	D,(HL)	56	1	7	TAY LDA (zl,X) STA zc TYA	6	13
LD	D,(IX+byte)	DD 56 byte	3	19	PHA LDY #byte LDA (zx),Y STA ze+1 PLA	8	17-18
LD	D,(IY+byte)	FD 56 byte	3	19	PHA LDY #byte LDA (zy),Y STA ze+1 PLA	8	17-18
LD	E,A	5F	1	4	STA ze	2	3
LD	E,B	58	1	4	LDY zc+1 STY ze	4	6
LD	E,C	59	1	4	LDY zc STY ze	4	6
LD	E,D	5A	1	4	LDY ze+1 STY ze	4	6
LD	E,E	5B	1	4	NOP	1	2
LD	E,H	5C	1	4	LDY zl+1 STY ze	4	6
LD	E,L	5D	1	4	LDY zl STY ze	4	6
LD	E,(HL)	5E	1	7	TAY LDA (zl,X) STA ze TYA	6	13
LD	E,(IX+byte)	DD 5E byte	3	19	PHA LDY #byte LDA (zx),Y STA ze PLA	8	17-18
LD	E,(IY+byte)	FD 5E byte	3	19	PHA LDY #byte LDA (zy),Y STA ze PLA	8	17-18
LD	H,A	67	1	4	STA zl+1	2	3
LD	H,B	60	1	4	LDY zc+1 STY zl+1	4	6
LD	H,C	61	1	4	LDY zc STY zl+1	4	6
LD	H,D	62	1	4	LDY ze+1 STY zl+1	4	6
LD	H,E	63	1	4	LDY ze STY zl+1	4	6
LD	H,H	64	1	4	NOP	1	2
LD	H,L	65	1	4	LDY zl STY zl+1	4	6
LD	H,(HL)	66	1	7	TAY LDA (zl,X) STA zl+1 TYA	6	13
LD	H,(IX+byte)	DD 66 byte	3	19	PHA LDY #byte LDA (zx),Y STA zl+1 PLA	8	17-18
LD	H,(IY+byte)	FD 66 byte	3	19	〃	8	17-18
LD	L,A	6F	1	4	STA zl	2	3
LD	L,B	68	1	4	LDY zc+1 STY zl	4	6
LD	L,C	69	1	4	LDY zc STY zl	4	6
LD	L,D	6A	1	4	LDY ze+1 STY zl	4	6
LD	L,E	6B	1	4	LDY ze STY zl	4	6
LD	L,H	6C	1	4	LDY zl+1 STY zl	4	6
LD	L,L	6D	1	4	NOP	1	2
LD	L,(HL)	6E	1	7	TAY LDA (zl,X) STA zl TYA	6	13
LD	L,(IX+byte)	DD 6E byte	3	19	PHA LDY #byte LDA (zx),Y STA zl PLA	8	17-18
LD	L,(IY+byte)	FD 6E byte	3	19	〃	8	17-18
LD	A,byte	3E byte	2	7	LDA #byte	2	2
LD	B,byte	06 byte	2	7	LDY #byte STY zc+1	4	5
LD	C,byte	0E byte	2	7	LDY #byte STY zc	4	5
LD	D,byte	16 byte	2	7	LDY #byte STY ze+1	4	5
LD	E,byte	1E byte	2	7	LDY #byte STY ze	4	5
LD	H,byte	26 byte	2	7	LDY #byte STY zl+1	4	5
LD	L,byte	2E byte	2	7	LDY #byte STY zl	4	5
LD	(HL),byte	36 byte	2	10	TAY LDA #byte STA (zl,X) TYA	6	12
LD	(IX+byte),A	DD 77 byte	3	19	LDY #byte STA (zx,Y)	4	8
LD	(IX+byte),B	DD 70 byte	3	19	PHA LDY #byte LDA zc+1 STA (zx),Y PLA	8	18
LD	(IX+byte),C	DD 71 byte	3	19	PHA LDY #byte LDA zc STA (zx),Y PLA	8	18
LD	(IX+byte),D	DD 72 byte	3	19	〃	8	18
LD	(IX+byte),E	DD 73 byte	3	19	〃	8	18
LD	(IX+byte),H	DD 74 byte	3	19	〃	8	18
LD	(IX+byte),L	DD 75 byte	3	19	〃	8	18
LD	(IX+byte1),byte2	DD 36 byte1 byte2	3	19	PHA LDY #byte1 LDA #byte2 STA (zx),Y PLA	8	17
LD	(IY+byte),A	FD 77 byte	3	19	LDY #byte STA (zy,Y)	4	8
LD	(IY+byte),B	FD 70 byte	3	19	PHA LDY #byte LDA zc+1 STA (zy),Y PLA	8	18
LD	(IY+byte),C	FD 71 byte	3	19	〃	8	18
LD	(IY+byte),D	FD 72 byte	3	19	〃	8	18
LD	(IY+byte),E	FD 73 byte	3	19	〃	8	18
LD	(IY+byte),H	FD 74 byte	3	19	〃	8	18
LD	(IY+byte),L	FD 75 byte	3	19	〃	8	18
LD	(IY+byte1),byte2	FD 36 byte1 byte2	3	19	PHA LDY #byte1 LDA #byte2 STA (zy),Y PLA	8	17
LD	A,I	ED 57	2	9
LD	I,A	ED 47	2	9
LD	A,R	ED 5F	2	9
LD	R,A	ED 4F	2	9
LD	(BC),A	02	1	7	STA (zc,X)	2	6
LD	(DE),A	12	1	7	STA (ze,X)	2	6
LD	(word),A	32	3	13	STA word	3	4
LD	BC,word	01 word	3	10	LDY #wordlo STY zc LDY #wordhi STY zc+1	8	10
LD	DE,word	11 word	3	10	LDY #wordlo STY ze LDY #wordhi STY ze+1	8	10
LD	HL,word	21 word	3	10	LDY #wordlo STY zl LDY #wordhi STY zl+1	8	10
LD	SP,word	31 word	3	10	LDX #wordlo TXS LDX #0	5	6
LD	IX,word	DD 21 word	4	14	LDY #wordlo STY zx LDY #wordhi STY zx+1	8	10
LD	IY,word	FD 21 word	4	14	LDY #wordlo STY zy LDY #wordhi STY zy+1	8	10
LD	HL,(word)	2A word	3	16	LDY word STY zl LDY word+1 STY zl+1	10-12	12-14
LD	BC,(word)	ED 4B word	4	20	〃	10-12	12-14
LD	DE,(word)	ED 5B word	4	20	〃	10-12	12-14
LD	HL,(word)	ED 6B word	4	20	〃	10-12	12-14	a duplicate
LD	IX,(word)	DD 2A word	4	20	〃	10-12	12-14
LD	IY,(word)	FD 2A word	4	20	〃	10-12	12-14
LD	SP,(word)	ED 7B word	4	20	LDX word TXS LDX #0	5-6	7-8
LD	(word),HL	22 word	3	16	LDY zl STY word LDY zl+1 STY word+1	10-12	12-14
LD	(word),BC	ED 43 word	4	20	〃	10-12	12-14
LD	(word),DE	ED 53 word	4	20	〃	10-12	12-14
LD	(word),HL	ED 63 word	4	20	〃	10-12	12-14	a duplicate
LD	(word),IX	DD 22 word	4	20	〃	10-12	12-14
LD	(word),IY	FD 22 word	4	20	〃	10-12	12-14
LD	(word),SP	ED 73 word	4	20	TSX STX word LDX #0	5-6	7-8
LD	SP,HL	F9	1	6	LDX zl TXS LDX #0	5	6
LD	SP,IX	DD F9	2	10	LDX zx TXS LDX #0	5	6
LD	SP,IY	FD F9	2	10	〃	5	6
EX	DE,HL	EB	1	4	LDX ze LDY zl STX zl STY ze LDX ze+1 LDY zl+1 STX zl+1 STY ze+1 LDX #0	18	26
EX	(SP),HL	E3	1	19	PHA TSX LDY $103,X LDA zl+1 STY zl+1 STA $103,X LDY $102,X LDA zl STY zl STA $102,X LDX #0 PLA	25	39
EX	(SP),IX	DD E3	2	23	〃	25	39
EX	(SP),IY	FD E3	2	23	〃	25	39
EX	AF,AF'	08	1	4	PHP LDY zaf+1 STA zaf+1 PLA LDX zaf STA zaf TXA PHA TYA LDX #0 PLP	16	32
EXX		D9	1	4	LDX zr1 LDY zr2 STX zr2 STY zr1 x6 LDX #0	50	74
LDI		ED A0	2	16	TAY LDA (zl,X) STA (ze,X) INC zl BNE $+4 INC zl+1 INC ze BNE $+4 INC ze+1 LDA zc BNE $+4 DEC zc+1 DEC zc TYA	26	43-55
LDD		ED A8	2	16	TAY LDA (zl,X) STA (ze,X) LDA zl BNE $+4 DEC zl+1 DEC zl LDA ze BNE $+4 DEC ze+1 DEC ze LDA zc BNE $+4 DEC zc+1 DEC zc TYA	30	49-61
LDIR		ED B0	2	21n-5	PHA LDY #0 loop LDA (zl),Y STA (ze),Y INY BNE $+6 INC zl+1 INC ze+1 LDA zc BNE $+4 DEC zc+1 DEC zc BNE loop LDA zc+1 BNE loop CLC TYA ADC zl STA zl BCC $+4 INC zl+1 CLC TYA ADC ze STA ze BCC $+4 INC ze+1 PLA	51	(30-31)n+43
LDDR		ED B8	2	21n-5	PHA LDY #0 loop LDA (zl),Y STA (ze),Y TYA BNE $+6 DEC zl+1 DEC ze+1 DEY LDA zc BNE $+4 DEC zc+1 DEC zc BNE loop LDA zc+1 BNE loop STY zs SEC LDA zl SBC zs STA zl BCS $+4 DEC zl+1 SEC LDA ze SBC zs STA ze BCS $+4 DEC ze+1 PLA	56	(32-33)n+48
PUSH	BC	C5	1	11	TAY LDA zc PHA LDA zc+1 PHA TYA	8	16
PUSH	DE	D5	1	11	〃	8	16
PUSH	HL	E5	1	11	〃	8	16
PUSH	AF	F5	1	11	PHP PHA	2	6
PUSH	IX	DD E5	2	15	TAY LDA zx PHA LDA zx+1 PHA TYA	8	16
PUSH	IY	FD E5	2	15	〃	8	16
POP	BC	C1	1	10	TAY PLA STA zc+1 PLA STA zc TYA	8	18
POP	DE	D1	1	10	〃	8	18
POP	HL	E1	1	10	〃	8	18
POP	AF	F1	1	10	PLA PLP	2	8
POP	IX	DD E1	2	14	TAY PLA STA zx+1 PLA STA zx TYA	8	18
POP	IY	FD E1	2	14	〃	8	18
ADD	A,A	87	1	4	ASL	1	2
ADD	A,B	80	1	4	CLC ADC zc+1	3	5
ADD	A,C	81	1	4	CLC ADC zc	3	5
ADD	A,D	82	1	4	CLC ADC ze+1	3	5
ADD	A,E	83	1	4	CLC ADC ze	3	5
ADD	A,H	84	1	4	CLC ADC zl+1	3	5
ADD	A,L	85	1	4	CLC ADC zl	3	5
ADD	A,(HL)	86	1	7	CLC ADC (zl,X)	3	8
ADD	A,(IX+byte)	DD 86 byte	3	19	CLC LDY #byte ADC (zx),Y	5	9-10
ADD	A,(IY+byte)	FD 86 byte	3	19	CLC LDY #byte ADC (zy),Y	5	9-10
ADD	A,byte	C6 byte	2	7	CLC ADC #byte	3	4
ADD	HL,BC	09	1	11	TAY CLC LDA zl ADC zc STA zl LDA zl+1 ADC zc+1 STA zl+1 TYA	15	24
ADD	HL,DE	19	1	11	〃	15	24
ADD	HL,HL	29	1	11	ASL zl ROL zl+1	6	10
ADD	HL,SP	39	1	11	TAY TSX TXA CLC ADC zl STA zl BCC $+4 INC zl+1 LDX #0 TYA	15	21/25
ADD	IX,BC	DD 09	2	15	TAY CLC LDA zl ADC zc STA zx LDA zl+1 ADC zc+1 STA zx+1 TYA	15	24
ADD	IX,DE	DD 19	2	15	〃	15	24
ADD	IX,HL	DD 29	2	15	〃	15	24
ADD	IX,SP	DD 39	2	15	TAY TSX TXA CLC ADC zx STA zx BCC $+4 INC zl+1 LDX #0 TYA	15	21/25
ADD	IY,BC	FD 09	2	15	TAY CLC LDA zl ADC zc STA zy LDA zl+1 ADC zc+1 STA zy+1 TYA	15	24
ADD	IY,DE	FD 19	2	15	〃	15	24
ADD	IY,HL	FD 29	2	15	〃	15	24
ADD	IY,SP	DD 39	2	15	TAY TSX TXA CLC ADC zy STA zy BCC $+4 INC zl+1 LDX #0 TYA	15	21/25
ADC	A,A	8F	1	4	ROL	1	2
ADC	A,B	88	1	4	ADC zc+1	2	3
ADC	A,C	89	1	4	ADC zc	2	3
ADC	A,D	8A	1	4	ADC ze+1	3	5
ADC	A,E	8B	1	4	ADC ze	2	3
ADC	A,H	8C	1	4	ADC zl+1	2	3
ADC	A,L	8D	1	4	ADC zl	2	3
ADC	A,(HL)	8E	1	7	ADC (zl,X)	2	6
ADC	A,(IX+byte)	DD 8E byte	3	19	LDY #byte ADC (zx),Y	4	7-8
ADC	A,(IY+byte)	FD 8E byte	3	19	LDY #byte ADC (zy),Y	4	7-8
ADC	A,byte	CE byte	2	7	ADC #byte	2	2
ADC	HL,BC	ED 4A	2	15	TAY LDA zl ADC zc STA zl LDA zl+1 ADC zc+1 STA zl+1 TYA	14	22
ADC	HL,DE	ED 5A	2	15	〃	14	22
ADC	HL,HL	ED 6A	2	15	ASL zl ROL zl+1	6	10
ADC	HL,SP	ED 7A	2	15	TAY TSX TXA ADC zl STA zl BCC $+4 INC zl+1 LDX #0 TYA	14	19/23
SUB	A	97	1	4	AND #0	2	2
SUB	B	90	1	4	SEC SBC zc+1	3	5
SUB	C	91	1	4	SEC SBC zc	3	5
SUB	D	92	1	4	SEC SBC ze+1	3	5
SUB	E	93	1	4	SEC SBC ze	3	5
SUB	H	94	1	4	SEC SBC zl+1	3	5
SUB	L	95	1	4	SEC SBC zl	3	5
SUB	(HL)	96	1	7	SEC SBC (zl,X)	3	8
SUB	(IX+byte)	DD 96 byte	3	19	SEC LDY #byte SBC (zx),Y	5	9-10
SUB	(IY+byte)	FD 96 byte	3	19	SEC LDY #byte SBC (zy),Y	5	9-10
SUB	byte	D6 byte	2	7	SEC SBC #byte	3	4
SBC	A,A	9F	1	4	STA zs SBC zc	4	6
SBC	A,B	98	1	4	SBC zc+1	2	3
SBC	A,C	99	1	4	SBC zc	2	3
SBC	A,D	9A	1	4	SBC ze+1	2	3
SBC	A,E	9B	1	4	SBC ze	2	3
SBC	A,H	9C	1	4	SBC zl+1	2	3
SBC	A,L	9D	1	4	SBC zl	2	3
SBC	A,(HL)	9E	1	7	SBC (zl,X)	2	6
SBC	A,(IX+byte)	DD 9E byte	3	19	LDY #byte SBC (zx),Y	4	7-8
SBC	A,(IY+byte)	FD 9E byte	3	19	LDY #byte SBC (zy),Y	4	7-8
SBC	A,byte	DE byte	2	7	SBC #byte	2	2
SBC	HL,BC	ED 42	2	15	TAY LDA zl SBC zc STA zl LDA zl+1 SBC zc+1 STA zl+1 TYA	14	22
SBC	HL,DE	ED 52	2	15	〃	14	22
SBC	HL,HL	ED 62	2	15	TAY STA zs SBC zs STA zl STA zl+1 TYA	10	16
SBC	HL,SP	ED 72	2	15	TAY TSX STX zs LDX #0 LDA zl SBC zs STA zl BCS $+4 DEC zl+1 TYA	17	22/26
INC	A	3C	1	4	CLC ADC #1	3	4
INC	B	04	1	4	INC zc+1	2	5
INC	C	0C	1	4	INC zc	2	5
INC	D	14	1	4	INC ze+1	2	5
INC	E	1C	1	4	INC ze	2	5
INC	H	24	1	4	INC zl+1	2	5
INC	L	2C	1	4	INC zl	2	5
INC	(HL)	34	1	11	TAY LDA (zl,X) CLC ADC #1 STA (zl,X) TYA	9	20
INC	(IX+byte)	DD 34 byte	3	23	PHA LDY #byte LDA (zx),Y CLC ADC #1 STA (zx),Y PLA	11	22-23
INC	(IY+byte)	FD 34 byte	3	23	PHA LDY #byte LDA (zy),Y CLC ADC #1 STA (zy),Y PLA	11	22-23
INC	BC	03	1	6	INC zc BNE $+4 INC zc+1	6	8
INC	DE	13	1	6	INC ze BNE $+4 INC ze+1	6	8
INC	HL	23	1	6	INC zl BNE $+4 INC zl+1	6	8
INC	SP	33	1	6	TSX INX TXS LDX #0	5	8
INC	IX	DD 23	2	10	INC zx BNE $+4 INC zx+1	6	8
INC	IY	FD 23	2	10	INC zy BNE $+4 INC zy+1	6	8
DEC	A	3D	1	4	CLC SBC #0	3	4
DEC	B	05	1	4	DEC zc+1	2	5
DEC	C	0D	1	4	DEC zc	2	5
DEC	D	15	1	4	DEC ze+1	2	5
DEC	E	1D	1	4	DEC ze	2	5
DEC	H	25	1	4	DEC zl+1	2	5
DEC	L	2D	1	4	DEC zl	2	5
DEC	(HL)	35	1	11	TAY LDA (zl,X) SEC SBC #1 STA (zl,X) TYA	9	20
DEC	(IX+byte)	DD 35 byte	3	23	PHA LDY #byte LDA (zx),Y SEC SBC #1 STA (zx),Y PLA	11	22-23
DEC	(IY+byte)	FD 35 byte	3	23	PHA LDY #byte LDA (zy),Y SEC SBC #1 STA (zy),Y PLA	11	22-23
DEC	BC	0B	1	6	LDY zc BNE $+4 DEC zc+1 DEC zc	8	11
DEC	DE	1B	1	6	LDY ze BNE $+4 DEC ze+1 DEC ze	8	11
DEC	HL	2B	1	6	LDY zl BNE $+4 DEC zl+1 DEC zl	8	11
DEC	SP	3B	1	6	TSX DEX TXS LDX #0	5	8
DEC	IX	DD 2B	2	10	LDY zx BNE $+4 DEC zx+1 DEC zx	8	11
DEC	IY	FD 2B	2	10	LDY zy BNE $+4 DEC zy+1 DEC zy	8	11
CP	A	BF	1	4	LDX #0 SEC	3	4
CP	B	B8	1	4	CMP zc+1	3	3
CP	C	B9	1	4	CMP zc	3	3
CP	D	BA	1	4	CMP ze+1	3	3
CP	E	BB	1	4	CMP ze	3	3
CP	H	BC	1	4	CMP zl+1	3	3
CP	L	BD	1	4	CMP zl	3	3
CP	(HL)	BE	1	7	CMP (zl,X)	2	6
CP	(IX+byte)	DD BE byte	3	19	LDY #byte CMP (zx),Y	4	7-8
CP	(IY+byte)	FD BE byte	3	19	LDY #byte CMP (zy),Y	4	7-8
CP	byte	FE byte	2	7	CMP #byte	2	2
CPI		ED A1	2	16	CMP (zl,X) PHP INC zl BNE $+4 INC zl+1 LDY zc BNE $+4 DEC zc+1 DEC zc PLP	18	32
CPD		ED A9	2	16	CMP (zl,X) PHP LDY zl BNE $+4 DEC zl+1 DEC zl LDY zc BNE $+4 DEC zc+1 DEC zc PLP	24	41
CPIR		ED B1	2	21n-5	loop CMP (zl,X) PHP INC zl BNE $+4 INC zl+1 LDY zc BNE $+4 DEC zc+1 DEC zc PLP BNE exit LDY zc BNE loop LDY zc+1 BNE loop exit	28	40n-5
CPDR		ED B9	2	21n-5	loop CMP (zl,X) PHP LDY zl BNE $+4 INC zl+1 DEC zl LDY zc BNE $+4 DEC zc+1 DEC zc PLP BNE exit LDY zc BNE loop LDY zc+1 BNE loop exit	30	43n-5
AND	A	A7	1	4	ORA #0	2	2
AND	B	A0	1	4	AND zc+1	3	3
AND	C	A1	1	4	AND zc	3	3
AND	D	A2	1	4	AND ze+1	3	3
AND	E	A3	1	4	AND ze	3	3
AND	H	A4	1	4	AND zl+1	3	3
AND	L	A5	1	4	AND zl	3	3
AND	(HL)	A6	1	7	AND (zl,X)	2	6
AND	(IX+byte)	DD A6 byte	3	19	LDY #byte AND (zx),Y	4	7-8
AND	(IY+byte)	FD A6 byte	3	19	LDY #byte AND (zy),Y	4	7-8
AND	byte	E6 byte	2	7	AND #byte	2	2
OR	A	B7	1	4	ORA #0	2	2
OR	B	B0	1	4	ORA zc+1	3	3
OR	C	B1	1	4	ORA zc	3	3
OR	D	B2	1	4	ORA ze+1	3	3
OR	E	B3	1	4	ORA ze	3	3
OR	H	B4	1	4	ORA zl+1	3	3
OR	L	B5	1	4	ORA zl	3	3
OR	(HL)	B6	1	7	ORA (zl,X)	2	6
OR	(IX+byte)	DD B6 byte	3	19	LDY #byte OR (zx),Y	4	7-8
OR	(IY+byte)	FD B6 byte	3	19	LDY #byte OR (zy),Y	4	7-8
OR	byte	F6 byte	2	7	ORA #byte	2	2
XOR	A	AF	1	4	LDA #0	2	2
XOR	B	A8	1	4	EOR zc+1	3	3
XOR	C	A9	1	4	EOR zc	3	3
XOR	D	AA	1	4	EOR ze+1	3	3
XOR	E	AB	1	4	EOR ze	3	3
XOR	H	AC	1	4	EOR zl+1	3	3
XOR	L	AD	1	4	EOR zl	3	3
XOR	(HL)	AE	1	7	EOR (zl,X)	2	6
XOR	(IX+byte)	DD AE byte	3	19	LDY #byte XOR (zx),Y	4	7-8
XOR	(IY+byte)	FD AE byte	3	19	LDY #byte XOR (zy),Y	4	7-8
XOR	byte	E6 byte	2	7	EOR #byte	2	2
RLCA		07	1	4	TAY ASL TYA ROL	4	8
RRCA		0F	1	4	TAY LSR TYA ROR	4	8
RRA		17	1	4	ROL	1	2
RLA		1F	1	4	ROR	1	2
RLC	A	CB 07	2	8	TAY ASL TYA ROL	4	8	a duplicate
RLC	B	CB 00	2	8	TAY LDA zc ASL TYA ROL zc	7	12
RLC	C	CB 01	2	8	〃	7	12
RLC	D	CB 02	2	8	〃	7	12
RLC	E	CB 03	2	8	〃	7	12
RLC	H	CB 04	2	8	〃	7	12
RLC	L	CB 05	2	8	〃	7	12
RLC	(HL)	CB 06	2	15	PHA LDA (zl,X) TAY ASL TYA ROL STA (zl,X) PLA	11	25
RLC	(IX+byte)	DD CB byte 06	4	23	PHA LDY #byte LDA (zx),Y TAX ASL TXA ROL STA (zx),Y LDX #0 PLA	14	30-31
RLC	(IY+byte)	FD CB byte 06	4	23	〃	14	30-31
RRC	A	CB 0F	2	8	TAY LSR TYA ROR	4	8	a duplicate
RRC	B	CB 08	2	8	TAY LDA zc+1 LSR TYA ROR zc+1	7	12
RRC	C	CB 09	2	8	〃	7	12
RRC	D	CB 0A	2	8	〃	7	12
RRC	E	CB 0B	2	8	〃	7	12
RRC	H	CB 0C	2	8	〃	7	12
RRC	L	CB 0D	2	8	〃	7	12
RRC	(HL)	CB 0E	2	15	PHA LDA (zl,X) TAY LSR TYA ROR STA (zl,X) PLA	11	25
RRC	(IX+byte)	DD CB byte 0E	4	23	PHA LDY #byte LDA (zx),Y TAX ASL TXA ROL STA (zx),Y LDX #0 PLA	14	30-31
RRC	(IY+byte)	FD CB byte 0E	4	23	〃	14	30-31
RL	A	CB 17	2	8	ROL	1	2	a duplicate
RL	B	CB 10	2	8	ROL zc+1	2	5
RL	C	CB 11	2	8	ROL zc	2	5
RL	D	CB 12	2	8	ROL ze+1	2	5
RL	E	CB 13	2	8	ROL ze	2	5
RL	H	CB 14	2	8	ROL zl+1	2	5
RL	L	CB 15	2	8	ROL zl	2	5
RL	(HL)	CB 16	2	15	TAY LDA (zl,X) ROL STA (zl,X) TYA	7	18
RL	(IX+byte)	DD CB byte 16	4	23	PHA LDY #byte LDA (zx),Y ROL STA (zx),Y PLA	9	22-23
RL	(IY+byte)	FD CB byte 16	4	23	〃	9	22-23
RR	A	CB 1F	2	8	ROR	1	2	a duplicate
RR	B	CB 18	2	8	ROR zc+1	2	5
RR	C	CB 19	2	8	ROR zc	2	5
RR	D	CB 1A	2	8	ROR ze+1	2	5
RR	E	CB 1B	2	8	ROR ze	2	5
RR	H	CB 1C	2	8	ROR zl+1	2	5
RR	L	CB 1D	2	8	ROR zl	2	5
RR	(HL)	CB 1E	2	15	TAY LDA (zl,X) ROR STA (zl,X) TYA	7	18
RR	(IX+byte)	DD CB byte 1E	4	23	PHA LDY #byte LDA (zx),Y ROR STA (zx),Y PLA	9	22-23
RR	(IY+byte)	FD CB byte 1E	4	23	〃	9	22-23
SLA	A	CB 27	2	8	ASL	1	2
SLA	B	CB 20	2	8	ASL zc+1	2	5
SLA	C	CB 21	2	8	ASL zc	2	5
SLA	D	CB 22	2	8	ASL ze+1	2	5
SLA	E	CB 23	2	8	ASL ze	2	5
SLA	H	CB 24	2	8	ASL zl+1	2	5
SLA	L	CB 25	2	8	ASL zl	2	5
SLA	(HL)	CB 26	2	15	TAY LDA (zl,X) ASL STA (zl,X) TYA	7	18
SLA	(IX+byte)	DD CB byte 26	4	23	PHA LDY #byte LDA (zx),Y ASL STA (zx),Y PLA	9	22-23
SLA	(IY+byte)	FD CB byte 26	4	23	〃	9	22-23
SRL	A	CB 3F	2	8	LSR	1	2
SRL	B	CB 38	2	8	LSR zc+1	2	5
SRL	C	CB 39	2	8	LSR zc	2	5
SRL	D	CB 3A	2	8	LSR ze+1	2	5
SRL	E	CB 3B	2	8	LSR ze	2	5
SRL	H	CB 3C	2	8	LSR zl+1	2	5
SRL	L	CB 3D	2	8	LSR zl	2	5
SRL	(HL)	CB 3E	2	15	TAY LDA (zl,X) LSR STA (zl,X) TYA	7	18
SRL	(IX+byte)	DD CB byte 3E	4	23	PHA LDY #byte LDA (zx),Y LSR STA (zx),Y PLA	9	22-23
SRL	(IY+byte)	FD CB byte 3E	4	23	〃	9	22-23
SRA	A	CB 2F	2	8	TAY ASL TYA ROR	4	8
SRA	B	CB 28	2	8	LDY zc+1 CLC BPL $+3 SEC ROR zc+1	8	13-14
SRA	C	CB 29	2	8	〃	8	13-14
SRA	D	CB 2A	2	8	〃	8	13-14
SRA	E	CB 2B	2	8	〃	8	13-14
SRA	H	CB 2C	2	8	〃	8	13-14
SRA	L	CB 2D	2	8	〃	8	13-14
SRA	(HL)	CB 2E	2	15	TAY LDA (zl,X) CLC BPL $+3 SEC ROR STA (zl,X) TYA	11	23-24
SRA	(IX+byte)	DD CB byte 2E	4	23	PHA LDY #byte LDA (zx),Y CLC BPL $+3 SEC ROR STA (zx),Y PLA	13	27-29
SRA	(IY+byte)	FD CB byte 2E	4	23	〃	13	27-29
RLD		ED 6F	2	18	PHA LDA (zl,X) TAY LSR x4 STA zs+1 TYA ASL x4 STA zs PLA TAY AND #F OR zs STA (zl,X) TYA AND #F0 OR zs+1	59	30
RRD		ED 67	2	18	PHA LDA (zl,X) TAY AND #F STA zs+1 TYA AND #F0 STA zs PLA TAY AND #F OR zs STA (zl,X) TYA AND #F0 OR zs+1 ROL x4	55	28
BIT	0,A	CB 47	2	8	LDY #1 STY zs BIT zs	6	8
BIT	1,A	CB 4F	2	8	LDY #2 STY zs BIT zs	6	8
BIT	2,A	CB 57	2	8	LDY #4 STY zs BIT zs	6	8
BIT	3,A	CB 5F	2	8	LDY #8 STY zs BIT zs	6	8
BIT	4,A	CB 67	2	8	LDY #10 STY zs BIT zs	6	8
BIT	5,A	CB 6F	2	8	〃	6	8
BIT	6,A	CB 77	2	8	〃	6	8
BIT	7,A	CB 7F	2	8	〃	6	8
BIT	0,B	CB 40	2	8	TAY LDA #1 BIT zc+1 PHP TYA PLP	8	16
BIT	1,B	CB 48	2	8	〃	8	16
BIT	2,B	CB 50	2	8	〃	8	16
BIT	3,B	CB 58	2	8	〃	8	16
BIT	4,B	CB 60	2	8	〃	8	16
BIT	5,B	CB 68	2	8	〃	8	16
BIT	6,B	CB 70	2	8	〃	8	16
BIT	7,B	CB 78	2	8	〃	8	16
BIT	0,C	CB 41	2	8	TAY LDA #1 BIT zc PHP TYA PLP	8	16
BIT	1,C	CB 49	2	8	〃	8	16
BIT	2,C	CB 51	2	8	〃	8	16
BIT	3,C	CB 59	2	8	〃	8	16
BIT	4,C	CB 61	2	8	〃	8	16
BIT	5,C	CB 69	2	8	〃	8	16
BIT	6,C	CB 71	2	8	〃	8	16
BIT	7,C	CB 79	2	8	〃	8	16
BIT	0,D	CB 42	2	8	TAY LDA #1 BIT ze+1 PHP TYA PLP	8	16
BIT	1,D	CB 4A	2	8	〃	8	16
BIT	2,D	CB 52	2	8	〃	8	16
BIT	3,D	CB 5A	2	8	〃	8	16
BIT	4,D	CB 62	2	8	〃	8	16
BIT	5,D	CB 6A	2	8	〃	8	16
BIT	6,D	CB 72	2	8	〃	8	16
BIT	7,D	CB 7A	2	8	〃	8	16
BIT	0,E	CB 43	2	8	TAY LDA #1 BIT ze PHP TYA PLP	8	16
BIT	1,E	CB 4B	2	8	〃	8	16
BIT	2,E	CB 53	2	8	〃	8	16
BIT	3,E	CB 5B	2	8	〃	8	16
BIT	4,E	CB 63	2	8	〃	8	16
BIT	5,E	CB 6B	2	8	〃	8	16
BIT	6,E	CB 73	2	8	〃	8	16
BIT	7,E	CB 7B	2	8	〃	8	16
BIT	0,H	CB 44	2	8	TAY LDA #1 BIT zl+1 PHP TYA PLP	8	16
BIT	1,H	CB 4C	2	8	〃	8	16
BIT	2,H	CB 54	2	8	〃	8	16
BIT	3,H	CB 5C	2	8	〃	8	16
BIT	4,H	CB 64	2	8	〃	8	16
BIT	5,H	CB 6C	2	8	〃	8	16
BIT	6,H	CB 74	2	8	〃	8	16
BIT	7,H	CB 7C	2	8	〃	8	16
BIT	0,L	CB 45	2	8	TAY LDA #1 BIT zl PHP TYA PLP	8	16
BIT	1,L	CB 4D	2	8	〃	8	16
BIT	2,L	CB 55	2	8	〃	8	16
BIT	3,L	CB 5D	2	8	〃	8	16
BIT	4,L	CB 65	2	8	〃	8	16
BIT	5,L	CB 6D	2	8	〃	8	16
BIT	6,L	CB 75	2	8	〃	8	16
BIT	7,L	CB 7D	2	8	〃	8	16
BIT	0,(HL)	CB 46	2	12	TAY LDA #1 AND (zl,X) PHP TYA PLP	8	19
BIT	1,(HL)	CB 4E	2	12	〃	8	19
BIT	2,(HL)	CB 56	2	12	〃	8	19
BIT	3,(HL)	CB 5E	2	12	〃	8	19
BIT	4,(HL)	CB 66	2	12	〃	8	19
BIT	5,(HL)	CB 6E	2	12	〃	8	19
BIT	6,(HL)	CB 76	2	12	〃	8	19
BIT	7,(HL)	CB 7E	2	12	〃	8	19
BIT	0,(IX+byte)	DD CB byte 46	4	20	TAX LDY #byte LDA #1 AND (zx),Y PHP TXA LDX #0 PLP	12	22-23
BIT	1,(IX+byte)	DD CB byte 4E	4	20	〃	12	22-23
BIT	2,(IX+byte)	DD CB byte 56	4	20	〃	12	22-23
BIT	3,(IX+byte)	DD CB byte 5E	4	20	〃	12	22-23
BIT	4,(IX+byte)	DD CB byte 66	4	20	〃	12	22-23
BIT	5,(IX+byte)	DD CB byte 6E	4	20	〃	12	22-23
BIT	6,(IX+byte)	DD CB byte 76	4	20	〃	12	22-23
BIT	7,(IX+byte)	DD CB byte 7E	4	20	〃	12	22-23
BIT	0,(IY+byte)	FD CB byte 46	4	20	TAX LDY #byte LDA #1 AND (zy),Y PHP TXA LDX #0 PLP	12	22-23
BIT	1,(IY+byte)	FD CB byte 4E	4	20	〃	12	22-23
BIT	2,(IY+byte)	FD CB byte 56	4	20	〃	12	22-23
BIT	3,(IY+byte)	FD CB byte 5E	4	20	〃	12	22-23
BIT	4,(IY+byte)	FD CB byte 66	4	20	〃	12	22-23
BIT	5,(IY+byte)	FD CB byte 6E	4	20	〃	12	22-23
BIT	6,(IY+byte)	FD CB byte 76	4	20	〃	12	22-23
BIT	7,(IY+byte)	FD CB byte 7E	4	20	〃	12	22-23
SET	0,A	CB C7	2	8	OR #1	2	2
SET	1,A	CB CF	2	8	OR #2	2	2
SET	2,A	CB D7	2	8	OR #4	2	2
SET	3,A	CB DF	2	8	OR #8	2	2
SET	4,A	CB E7	2	8	OR #10	2	2
SET	5,A	CB EF	2	8	OR #20	2	2
SET	6,A	CB F7	2	8	OR #40	2	2
SET	7,A	CB FF	2	8	OR #80	2	2
SET	0,B	CB C0	2	8	TAY LDA #1 OR zc+1 STA zc+1 TYA	8	12
SET	1,B	CB C8	2	8	〃	8	12
SET	2,B	CB D0	2	8	〃	8	12
SET	3,B	CB D8	2	8	〃	8	12
SET	4,B	CB E0	2	8	〃	8	12
SET	5,B	CB E8	2	8	〃	8	12
SET	6,B	CB F0	2	8	〃	8	12
SET	7,B	CB F8	2	8	〃	8	12
SET	0,C	CB C1	2	8	TAY LDA #1 OR zc STA zc TYA	8	12
SET	1,C	CB C9	2	8	〃	8	12
SET	2,C	CB D1	2	8	〃	8	12
SET	3,C	CB D9	2	8	〃	8	12
SET	4,C	CB E1	2	8	〃	8	12
SET	5,C	CB E9	2	8	〃	8	12
SET	6,C	CB F1	2	8	〃	8	12
SET	7,C	CB F9	2	8	〃	8	12
SET	0,D	CB C2	2	8	TAY LDA #1 OR ze+1 STA ze+1 TYA	8	12
SET	1,D	CB CA	2	8	〃	8	12
SET	2,D	CB D2	2	8	〃	8	12
SET	3,D	CB DA	2	8	〃	8	12
SET	4,D	CB E2	2	8	〃	8	12
SET	5,D	CB EA	2	8	〃	8	12
SET	6,D	CB F2	2	8	〃	8	12
SET	7,D	CB FA	2	8	〃	8	12
SET	0,E	CB C3	2	8	TAY LDA #1 OR ze STA ze TYA	8	12
SET	1,E	CB CB	2	8	〃	8	12
SET	2,E	CB D3	2	8	〃	8	12
SET	3,E	CB DB	2	8	〃	8	12
SET	4,E	CB E3	2	8	〃	8	12
SET	5,E	CB EB	2	8	〃	8	12
SET	6,E	CB F3	2	8	〃	8	12
SET	7,E	CB FB	2	8	〃	8	12
SET	0,H	CB C4	2	8	TAY LDA #1 OR zl+1 STA zl+1 TYA	6	12
SET	1,H	CB CC	2	8	〃	8	12
SET	2,H	CB D4	2	8	〃	8	12
SET	3,H	CB DC	2	8	〃	8	12
SET	4,H	CB E4	2	8	〃	8	12
SET	5,H	CB EC	2	8	〃	8	12
SET	6,H	CB F4	2	8	〃	8	12
SET	7,H	CB FC	2	8	〃	8	12
SET	0,L	CB C5	2	8	TAY LDA #1 OR zl STA zl TYA	8	12
SET	1,L	CB CD	2	8	〃	8	12
SET	2,L	CB D5	2	8	〃	8	12
SET	3,L	CB DD	2	8	〃	8	12
SET	4,L	CB E5	2	8	〃	8	12
SET	5,L	CB ED	2	8	〃	8	12
SET	6,L	CB F5	2	8	〃	8	12
SET	7,L	CB FD	2	8	〃	8	12
SET	0,(HL)	CB C6	2	15	TAY LDA #1 OR (zl,X) STA (zl,X) TYA	8	18
SET	1,(HL)	CB CE	2	15	〃	8	18
SET	2,(HL)	CB D6	2	15	〃	8	18
SET	3,(HL)	CB DE	2	15	〃	8	18
SET	4,(HL)	CB E6	2	15	〃	8	18
SET	5,(HL)	CB EE	2	15	〃	8	18
SET	6,(HL)	CB F6	2	15	〃	8	18
SET	7,(HL)	CB FE	2	15	〃	8	18
SET	0,(IX+byte)	DD CB byte C6	4	23	PHA LDY #byte LDA #1 OR (zx),Y STA (zx),Y PLA	10	22-23
SET	1,(IX+byte)	DD CB byte CE	4	23	〃	10	22-23
SET	2,(IX+byte)	DD CB byte D6	4	23	〃	10	22-23
SET	3,(IX+byte)	DD CB byte DE	4	23	〃	10	22-23
SET	4,(IX+byte)	DD CB byte E6	4	23	〃	10	22-23
SET	5,(IX+byte)	DD CB byte EE	4	23	〃	10	22-23
SET	6,(IX+byte)	DD CB byte F6	4	23	〃	10	22-23
SET	7,(IX+byte)	DD CB byte FE	4	23	〃	10	22-23
SET	0,(IY+byte)	FD CB byte C6	4	23	PHA LDY #byte LDA #1 OR (zy),Y STA (zy),Y PLA	10	22-23
SET	1,(IY+byte)	FD CB byte CE	4	23	〃	10	22-23
SET	2,(IY+byte)	FD CB byte D6	4	23	〃	10	22-23
SET	3,(IY+byte)	FD CB byte DE	4	23	〃	10	22-23
SET	4,(IY+byte)	FD CB byte E6	4	23	〃	10	22-23
SET	5,(IY+byte)	FD CB byte EE	4	23	〃	10	22-23
SET	6,(IY+byte)	FD CB byte F6	4	23	〃	10	22-23
SET	7,(IY+byte)	FD CB byte FE	4	23	〃	10	22-23
RES	0,A	CB 87	2	8	AND #FE	2	2
RES	1,A	CB 8F	2	8	AND #FD	2	2
RES	2,A	CB 97	2	8	AND #FB	2	2
RES	3,A	CB 9F	2	8	AND #F7	2	2
RES	4,A	CB A7	2	8	AND #EF	2	2
RES	5,A	CB AF	2	8	AND #DF	2	2
RES	6,A	CB B7	2	8	AND #BF	2	2
RES	7,A	CB BF	2	8	AND #7F	2	2
RES	0,B	CB 80	2	8	TAY LDA #FE AND zc+1 STA zc+1 TYA	8	12
RES	1,B	CB 88	2	8	〃	8	12
RES	2,B	CB 90	2	8	〃	8	12
RES	3,B	CB 98	2	8	〃	8	12
RES	4,B	CB A0	2	8	〃	8	12
RES	5,B	CB A8	2	8	〃	8	12
RES	6,B	CB B0	2	8	〃	8	12
RES	7,B	CB B8	2	8	〃	8	12
RES	0,C	CB 81	2	8	TAY LDA #FE AND zc STA zc TYA	8	12
RES	1,C	CB 89	2	8	〃	8	12
RES	2,C	CB 91	2	8	〃	8	12
RES	3,C	CB 99	2	8	〃	8	12
RES	4,C	CB A1	2	8	〃	8	12
RES	5,C	CB A9	2	8	〃	8	12
RES	6,C	CB B1	2	8	〃	8	12
RES	7,C	CB B9	2	8	〃	8	12
RES	0,D	CB 82	2	8	TAY LDA #FE AND ze+1 STA ze+1 TYA	8	12
RES	1,D	CB 8A	2	8	〃	8	12
RES	2,D	CB 92	2	8	〃	8	12
RES	3,D	CB 9A	2	8	〃	8	12
RES	4,D	CB A2	2	8	〃	8	12
RES	5,D	CB AA	2	8	〃	8	12
RES	6,D	CB B2	2	8	〃	8	12
RES	7,D	CB BA	2	8	〃	8	12
RES	0,E	CB 83	2	8	TAY LDA #FE AND ze STA ze TYA	8	12
RES	1,E	CB 8B	2	8	〃	8	12
RES	2,E	CB 93	2	8	〃	8	12
RES	3,E	CB 9B	2	8	〃	8	12
RES	4,E	CB A3	2	8	〃	8	12
RES	5,E	CB AB	2	8	〃	8	12
RES	6,E	CB B3	2	8	〃	8	12
RES	7,E	CB BB	2	8	〃	8	12
RES	0,H	CB 84	2	8	TAY LDA #FE AND zl+1 STA zl+1 TYA	6	12
RES	1,H	CB 8C	2	8	〃	8	12
RES	2,H	CB 94	2	8	〃	8	12
RES	3,H	CB 9C	2	8	〃	8	12
RES	4,H	CB A4	2	8	〃	8	12
RES	5,H	CB AC	2	8	〃	8	12
RES	6,H	CB B4	2	8	〃	8	12
RES	7,H	CB BC	2	8	〃	8	12
RES	0,L	CB 85	2	8	TAY LDA #FE AND zl STA zl TYA	8	12
RES	1,L	CB 8D	2	8	〃	8	12
RES	2,L	CB 95	2	8	〃	8	12
RES	3,L	CB 9D	2	8	〃	8	12
RES	4,L	CB A5	2	8	〃	8	12
RES	5,L	CB AD	2	8	〃	8	12
RES	6,L	CB B5	2	8	〃	8	12
RES	7,L	CB BD	2	8	〃	8	12
RES	0,(HL)	CB 86	2	15	TAY LDA #FE AND (zl,X) STA (zl,X) TYA	8	18
RES	1,(HL)	CB 8E	2	15	〃	8	18
RES	2,(HL)	CB 96	2	15	〃	8	18
RES	3,(HL)	CB 9E	2	15	〃	8	18
RES	4,(HL)	CB A6	2	15	〃	8	18
RES	5,(HL)	CB AE	2	15	〃	8	18
RES	6,(HL)	CB B6	2	15	〃	8	18
RES	7,(HL)	CB BE	2	15	〃	8	18
RES	0,(IX+byte)	DD CB byte 86	4	23	PHA LDY #byte LDA #FE AND (zx),Y STA (zx),Y PLA	10	22-23
RES	1,(IX+byte)	DD CB byte 8E	4	23	〃	10	22-23
RES	2,(IX+byte)	DD CB byte 96	4	23	〃	10	22-23
RES	3,(IX+byte)	DD CB byte 9E	4	23	〃	10	22-23
RES	4,(IX+byte)	DD CB byte A6	4	23	〃	10	22-23
RES	5,(IX+byte)	DD CB byte AE	4	23	〃	10	22-23
RES	6,(IX+byte)	DD CB byte B6	4	23	〃	10	22-23
RES	7,(IX+byte)	DD CB byte BE	4	23	〃	10	22-23
RES	0,(IY+byte)	FD CB byte 86	4	23	PHA LDY #byte LDA #FE AND (zy),Y STA (zy),Y PLA	10	22-23
RES	1,(IY+byte)	FD CB byte 8E	4	23	〃	10	22-23
RES	2,(IY+byte)	FD CB byte 96	4	23	〃	10	22-23
RES	3,(IY+byte)	FD CB byte 9E	4	23	〃	10	22-23
RES	4,(IY+byte)	FD CB byte A6	4	23	〃	10	22-23
RES	5,(IY+byte)	FD CB byte AE	4	23	〃	10	22-23
RES	6,(IY+byte)	FD CB byte B6	4	23	〃	10	22-23
RES	7,(IY+byte)	FD CB byte BE	4	23	〃	10	22-23
SCF		37	1	4	SEC	1	2
CCF		3F	1	4	ROL EOR #1 ROR	3	6
DI		F3	1	4	SEI	1	2
EI		FB	1	4	CLI	1	2
NOP		00	1	4	NOP	1	2
HALT		76	1	4
IM	0	ED 46	2	8
IM	1	ED 56	2	8
IM	2	ED 5E	2	8
CPL		2F	1	4	EOR #FF	2	2
NEG		ED 44	2	4	CLC EOR #FF ADC #1	5	6
DAA		2F	1	4
JP	near	C3 word	3	10	JMP word	3	3
JP	far	C3 word	3	10	〃	3	3
JP	NZ,near	C2 word	3	10	BNE near	2	2/3-4
JP	NZ,far	C2 word	3	10	BEQ $+5 JMP far	5	3-4/5
JP	Z,near	C8 word	3	10	BEQ near	2	2/3-4
JP	Z,far	C8 word	3	10	BNE $+5 JMP word	5	3-4/5
JP	NC,near	D2 word	3	10	BCC near	2	2/3-4
JP	NC,far	D2 word	3	10	BCS $+5 JMP far	5	3-4/5
JP	C,near	D8 word	3	10	BCS near	2	2/3-4
JP	C,far	D8 word	3	10	BCC $+5 JMP far	5	3-4/5
JP	PO,near	E2 word	3	10	BVC near	2	2/3-4
JP	PO,far	E2 word	3	10	BVS $+5 JMP far	5	3-4/5
JP	PE,near	E8 word	3	10	BVS near	2	2/3-4
JP	PE,far	E8 word	3	10	BVC $+5 JMP far	5	3-4/5
JP	P,near	F2 word	3	10	BPL near	2	2/3-4
JP	P,far	F2 word	3	10	BMI $+5 JMP far	5	3-4/5
JP	M,near	F8 word	3	10	BMI near	2	2/3-4
JP	M,far	F8 word	3	10	BPL $+5 JMP far	5	3-4/5
JR	byte	18 byte	2	12	JMP word	3	3
JR	NC, byte	30 byte	2	7/12	BCC byte	2	2/3-4
JR	C, byte	38 byte	2	7/12	BCS byte	2	2/3-4
JR	NZ, byte	20 byte	2	7/12	BNE byte	2	2/3-4
JR	Z, byte	28 byte	2	7/12	BEQ byte	2	2/3-4
JP	(HL)	E9	1	4	JMP (zl)	3	5
JP	(IX)	DD E9	2	8	JMP (zx)	3	5
JP	(IY)	DD E9	2	8	JMP (zy)	3	5
DJNZ	near	10 byte	2	8/13	DEC zc+1 BNE near	4	7/8-9
CALL	word	CD word	3	17	JSR word	3	6
CALL	NZ,word	C4 word	3	10/17	BEQ $+5 JSR word	5	3-4/8
CALL	Z,word	CC word	3	10/17	BNE $+5 JSR word	5	3-4/8
CALL	NC,word	D4 word	3	10/17	BCS $+5 JSR word	5	3-4/8
CALL	C,word	DC word	3	10/17	BCC $+5 JSR word	5	3-4/8
CALL	PO,word	E4 word	3	10/17	BVS $+5 JSR word	5	3-4/8
CALL	PE,word	EC word	3	10/17	BVC $+5 JSR word	5	3-4/8
CALL	P,word	F4 word	3	10/17	BMI $+5 JSR word	5	3-4/8
CALL	M,word	FC word	3	10/17	BPL $+5 JSR word	5	3-4/8
RET		C9	1	10	RTS	1	6
RETI		ED 4D	2	14	RTI	1	6
RETN		ED 45	2	14
RET	NZ	C0	1	5/11	BEQ $+3 RTS	3	3-4/8
RET	Z	C8	1	5/11	BNE $+3 RTS	3	3-4/8
RET	NC	D0	1	5/11	BCS $+3 RTS	3	3-4/8
RET	C	D8	1	5/11	BCC $+3 RTS	3	3-4/8
RET	PO	E0	1	5/11	BVS $+3 RTS	3	3-4/8
RET	PE	E8	1	5/11	BVC $+3 RTS	3	3-4/8
RET	P	F0	1	5/11	BMI $+3 RTS	3	3-4/8
RET	M	F8	1	5/11	BPL $+3 RTS	3	3-4/8
RST	0	C7	1	11	BRK	1	7
RST	8	CF	1	11	BRK	1	7
RST	10	D7	1	11	BRK	1	7
RST	18	DF	1	11	BRK	1	7
RST	20	E7	1	11	BRK	1	7
RST	28	EF	1	11	BRK	1	7
RST	30	F7	1	11	BRK	1	7
RST	38	FF	1	11	BRK	1	7
IN	A,(byte)	DB byte	2	11
OUT	(byte),A	D3 byte	2	11
IN	A,(C)	ED 78	2	12
IN	B,(C)	ED 40	2	12
IN	C,(C)	ED 48	2	12
IN	D,(C)	ED 50	2	12
IN	E,(C)	ED 58	2	12
IN	H,(C)	ED 60	2	12
IN	L,(C)	ED 68	2	12
IN	(C)	ED 70	2	12
OUT	(C),A	ED 79	2	12
OUT	(C),B	ED 41	2	12
OUT	(C),C	ED 49	2	12
OUT	(C),D	ED 51	2	12
OUT	(C),E	ED 59	2	12
OUT	(C),H	ED 61	2	12
OUT	(C),L	ED 69	2	12
OUT	(C),0	ED 71	2	12
INI		ED A2	2	16
IND		ED AA	2	16
INIR		ED B2	2	21n-5
INDR		ED BA	2	21n-5
OUTI		ED A3	2	16
OUTD		ED AB	2	16
OTIR		ED B3	2	21n-5
OTDR		ED BB	2	21n-5

## Links to similar tables
- Modelling the 8080 and Z80 instructions on the 8088
- The Z80 and 8088 instructions for the additional 8085 instructions
## References
1. Mohamed Rafiquzzaman Microprocessors and Microcomputer Development Systems: Designing Microprocessor-Based Systems, Harper and Row, 1984
2. Commodore+4 info sheet

https://litwr2.github.io/8080-8085-z80-8088-6502/z80-6502.html